# SMS / text commands
Text commands can be issued by SMS, serial port (DIAG) or IP (App/Web/Perl). This overview does not cover all commands and details, please read the user guides for more info.
Notes:
- Disable automatic spelling correction.
- Ensure phone SMS encoding is set to 7 bit GSM (8 or 16 bit not supported).
- Use exactly one blank to separate arguments.
- Do not separate the „?“ from a query command (e.g. „SERVER?“).
- Case is irrelevant on commands (PASS = pass) but may be relevant on arguments (i.e. login, password, …).
- Wait for acknowledgement of each command sent before sending the next. If you get no reply, check spelling and try again.

## OVMS configuration
### Basic setup
Command	Function
REGISTER password	Register sending mobile phone as primary user (only SMS). Initial password is "OVMS".
PASS newpassword	Change REGISTER password (only from registered phone)
MODULE vehicleid units channels cartype	Set vehicle id (= server login), units ("M" / "K"), notification channels ("SMSIP") and car type ("RT") / Note: vehicle password set by SERVER command

### IP setup (GPRS)
Command	Function
GPRS apn apnuser apnpassword [dnsip]	Set APN config; use "-" for empty user/password/DNS / Note: DNS normally not needed
SERVER address vehiclepassword paranoidmode	Configure server connection; paranoidmode "-" or "P" (end-to-end encryption = server cannot decode data, no logs etc.) / Note: vehicle login set by MODULE command

### Troubleshooting
Command	Function
VERSION	Query firmware version
DIAG	Show LED and communication status (see "Network-State-Machine.pdf")
MODULE?	Query module config
GPRS?	Query APN config & GPRS status
SERVER?	Query server config & status
PARAMS?	Query all parameters
FEATURES?	Query all features
RESET	Restart the module

## Twizy configuration
### Range & charge alerts
Command	Function
RANGE maxrange	Set your max range (in user units) at 100% SOC & 20 °C
CA range	Set charge alert for sufficient range (in user units)
CA soc%	Set charge alert for sufficient SOC (note: "%" must be added)
CA range soc%	Set charge alert for sufficient range (in user units) and/or SOC
CA	Clear charge alerts

### Feature map
Command	Function
FEATURE 1 kickdownthreshold	Kickdown sensitivity (default 35, lower value = faster activation)
FEATURE 2 kickdowncompensation	Kickdown pedal compensation point (default 120)
FEATURE 8 gpsstreaming	0 = no location streaming, GPS log entry once per minute / 1 = location streaming every 2 seconds, GPS log entry per minute / 2 = no location streaming, GPS logging every 5 seconds / 3 = location streaming every 2 seconds, GPS logging every 5 seconds / If you don't need App streaming, mode 0 is perfect for normal resolution tracks, and mode 2 is perfect for high resolution track logging.
FEATURE 9 minsoc	Low SOC warning threshold (default: 0)
FEATURE 10 sufficientsoc	Charge notification by SOC (in %)
FEATURE 11 sufficientrange	Charge notification by range (in user unit)
FEATURE 12 maxrange	Range (in user units) at 100% SOC & 20 °C
FEATURE 13 batterycapacity	Running average (last 10 charges) capacity value (percentage), 0 = clear / Note: shown as integer, but stored as float
FEATURE 14 communicationflags	Communication control: add... / 2 = suppress "Access Denied" SMS / 4 = suppress all outbound SMS / 8 = suppress vehicle alerts / 16 = suppress vehicle info notifies / 32 = suppress times in SMS responses / 64 = send charge start notifications
FEATURE 15 canbusflags	CAN bus access control: add… / 1 = enable CAN write access / 2 = disable emergency CFG RESET / 4 = disable kickdown / 8 = disable auto power adjustment

## Twizy status

Command	Function
STAT?	Query battery state of charge (SOC) and capacity, range, charge status, odometer
GPS?	Query GPS position
TEMPS?	Query temperatures
CA?	Query charge alert setup (features 10+11), charge status & charge time estimations for alerts and full charge
RANGE?	Query max range setting in user units (feature 12)
POWER	Show power efficiency (trip report)
POWER T	Show power usage sums
BATT	Show battery alert and watch status
BATT V	Show battery voltage levels
BATT VD	Show battery cell voltage deviations
BATT T	Show battery temperatures
BATT TD	Show battery module temperature deviations

## SEVCON tuning
Notes:
- You need to enable CAN write access (FEATURE 15 1).
- Some commands use the STOP mode, the Twizy may signal that and beep, that's normal.
- If stuck in STOP mode, restart Twizy without entering GO, wait for 10-15 seconds.
- 3 successive CAN bus errors (for example pushing button D/N/R before GO) will cause an emergency CFG RESET. If your Twizy has a component problem or is used by inexperienced drivers, you may want to disable this by FEATURE 15 3.

### Macro settings
Macro commands automate the tuning process and can easily be reset.
Command	Function
CFG SPEED max_kph warn_kph	Set speed limit and warn level. / max_kph: 6..111, default 80 (T45: 45) / warn_kph: 6..111, default 89 (T45: 56) / Note: needs ON before GO
CFG POWER torque power_low power_high current	Set torque, power and current levels. With current: / torque: 10..254 (%), default 100 / power_low: 10..254 (%), default 100 / power_high: 10..254 (%), default 100 / current: 10..123 (%), default none / Note: needs ON before GO
CFG DRIVE powerlevel autopower_ref autopower_min kickdown_threshold kickdown_compensation	Set drive power level, optional auto power adjustment and kickdown parameters. / powerlevel: 10..100 (%), default 100 / autopower_ref: 0..250 (100 W), default 0/-1=off / autopower_min: 0..100 (%), default 0/-1=none / kickdown_threshold: 0..250, default 35 (= Feature #1) / kickdown_compensation: 0..250, default 120 (= Feature #2)
CFG RECUP neutral brake autopower_ref autopower_min	Set recuperation power levels, optional auto power adjustment. / neutral: 0..100 (%), default 18 (T45: 21) / brake: 0..100 (%), default = neutral% / autopower_ref: 0..250 (100 W), default 0/-1=off / autopower_min: 0..100 (%), default 0/-1=none
CFG RAMPS start accel decel neutral brake	Set rates of torque demand changes (higher means faster). / start: 1..250 (‰), default 40 (T45: 30) / accel: 1..100 (%), default 25 (T45: 21) / decel: 0..100 (%), default 20 / neutral: 0..100 (%), default 40 / brake: 0..100 (%), default 40
CFG RAMPL accel decel	Set rpm change limits for ramps. / accel: 1..100 (%), default 30 = 6000 rpm/s / decel: 0..100 (%), default 30 = 6000 rpm/s
CFG SMOOTH level	Set smoothing level. / level: 0..100 (%), default 70
CFG TSMAP map trq1@spd1 trq2@spd2 trq3@spd3 trq4@spd4	Change torque/speed maps. / map: D = Drive, N = Neutral braking, B = Footbraking / trq1..4: torque 0..100 (%) / spd1..4: speed 0..120 (kph) / Defaults: / D: 100@33 100@39 100@50 100@66 / N,B: 100@33 80@39 50@50 20@66 / Note: needs ON before GO
CFG RESET	Reset all macro settings to their default values. / Note: needs ON before GO (else partial)
CFG CLEAR	Clear the SEVCON fault & min/max logs.

### Profile management
A profile stores a combination of macro settings and can be loaded by command (or by button if using a SimpleConsole). The OVMS can store 3 custom profiles in EEPROM plus the current SEVCON working set in RAM.

Command	Function
CFG INFO	Output currently active profile slot# and working set parameters for these commands: / SPEED, POWER, DRIVE, RECUP, RAMPS, SMOOTH
CFG SAVE slot	Save the current working set into an EEPROM slot. / slot: 1..3
CFG LOAD slot	Load a profile slot into the current working set. / slot: 0..3, 0=factory default config, 1..3=custom profile
CFG RESET slot	Reset a profile slot to the default values. / slot: 1..3: reset EEPROM profile directly / ...else: reset working set
CFG GET slot	Get (download) a complete profile base64 encoded. / slot: 1..3: get EEPROM profile directly / ...else: get working set
CFG SET slot base64data	Set (upload) a complete profile from a base64 encoded string (counterpart to CFG GET). / slot: 1..3: set EEPROM profile directly, no SEVCON access / ...else: set working set & try to apply changes to SEVCON / base64data: encoded profile from CFG GET or cfgconv / ...omit/empty = RESET profile

Base64 web utilities:
- http://dexters-web.de/cfgconv
- http://dexters-web.de/cfgedit

### Temporary speed limits

Command	Function
LOCK kph	Immediately and persistently limit the maximum speed. If kph is lower than the default reverse speed (~10 kph), the reverse speed will also be limited.
UNLOCK	Clear the speed lock and reset maximum speed to the current profile configuration. If locked by valet mode, the valet trip length will be extended by 1 km but stay active.
VALET km	Activate valet mode and set the allowed trip length in km. Speed will be restricted to 6 kph when exceeding trip length. / Default trip length = 1 km.
UNVALET	Clear valet mode trip length restriction. If a speed lock is currently active, also clears the lock.

### Low level access
These commands provide direct access to the SEVCON configuration objects (SDO = service data object, see CANopen standard).
Att: no backup, no easy reset, note values or save logs!
Command	Function
CFG PRE	Enter pre-operational state ("STOP", needed for some SDOs). / Note: only necessary for few SDOs; see FAQ
CFG OP	Enter operational state. As an alternative, just switch the Twizy off for 2-3 seconds, then on again & wait for 10-15 seconds.
CFG READ index_hex subindex_hex	Read CANopen SDO object numerical contents (displays hexadecimal and decimal value). / index_hex: SDO address (hexadecimal) / subindex_hex: SDO field (hexadecimal)
CFG READS index_hex subindex_hex	Read CANopen SDO object string contents. / index_hex: SDO address (hexadecimal) / subindex_hex: SDO field (hexadecimal)
CFG WRITE index_hex subindex_hex value_dec	Write CANopen SDO object. / index_hex: SDO address (hexadecimal) / subindex_hex: SDO field (hexadecimal) / value_dec: new value (decimal)
CFG WRITEO index_hex subindex_hex value_dec	Write-only CANopen SDO object (i.e. no READ before write). / index_hex: SDO address (hexadecimal) / subindex_hex: SDO field (hexadecimal) / value_dec: new value (decimal)

### Low level examples

Command	Function
CFG READS 1008 0	Read SEVCON firmware name (string)
CFG READS 1009 0	Read SEVCON hardware version (string)
CFG READS 100A 0	Read SEVCON software version (string)
CFG READ 1018 3	Read SEVCON dictionary version (hex)
CFG WRITE 4623 03 0	Disable battery / BMS power protection (power limiter) / ATT: voids warranty on rented battery! / Activate auto power on DRIVE & RECUP to protect battery!
CFG WRITE 3813 12 5000	Disable SEVCON low SOC power cutback / Note: BMS protection still applies unless disabled, else use auto power on DRIVE to protect battery!
CFG READ 2870 06	Read current BMS discharge (=drive) power limit: / power_kW = {value_dec} over {256}
CFG READ 2870 07	Read current BMS charge (=recup) power limit: / power_kW = {65536 - value_dec} over {256}

See "Twizy-SDO-List.pdf" for a selection of relevant SDOs or SEVCON DVT master dictionary spreadsheet for complete SDO list & documentation.